## Slide 1
Pac-Man vs. Matlab
Optimization of Pac-Man strategies using Model Predictive Control
Identification and Optimal Control project– Professor Glielmo Luigi
Gargiulo Antonio – Giannotti Valentina – Grimaldi Emmanuel – Morghen Andrea
University of Naples Federico II – 6 July 2023

## Slide 2
Summary
Environment Model
  Maze model
  Markov chains idea
  Pac-Man model
  Ghost model
Control Strategy
  Pac-Man strategy
  Model Predictive Control
  Travel Salesman’s problem
  Dynamic programming in stochastic framework idea
Simulation Results and Conclusions
  Future developments
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 1
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 3
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 2
Optimization of Pac-Man strategies using Model Predictive Control
INTRODUCTION
Multiple-objective games
Control strategies generally used
Simplified version of the Pac-Man game in MATLAB
Pac-Man game

## Slide 4
MAZE MODEL
Matrix-based representation
Maze evolution
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 3
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 5
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 4
Optimization of Pac-Man strategies using Model Predictive Control
EVOLUTION AND PORTABILITY
POWER UP & PACMAN EFFECT IMPLEMENTATION
MULTI-AGENTS IMPLEMENTATION
The game scenario at the k-th step of the game is uniquely determined by the state of the maze matrix and its elements at that instant:
The game model we implemented turns out to be portable to larger mazes with advanced game features…

## Slide 6
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
MODELLING MAZE WITH MARKOV CHAIN
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 5
Optimization of Pac-Man strategies using Model Predictive Control
Another possible implementation might be to consider the evolution of the game as a sequence of equiprobable (or not) states of the maze matrix.
State transitions occur in function of the entry and the evolution
of the Ghost (stochastic W)
The system is described by:
Where is a stochastic process.
Computationally very onerous!
Example of an increasing exponential growth of cases in Markov Chains

## Slide 7
PAC-MAN MODEL
DYNAMIC EQUATIONS
Pac-Man Model
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 6
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 8
GHOST MODEL
DYNAMIC EQUATIONS
Ghost model
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 7
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 9
GHOST MODEL
Extraction of inputs from a cyclic, random choice among different patterns
Ghost model
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 8
Optimization of Pac-Man strategies using Model Predictive Control
How does ghost choose its input for each step?
Possible patterns:
1.
2.
3.
4.

## Slide 10
ALTERNATIVE GHOST MODEL
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 9
Optimization of Pac-Man strategies using Model Predictive Control
A possible alternative and more aggressive model for the ghost might be inspired by the predator-prey model.
A well-known example is the Markov chain of the fly and the spider: they move along a straight line in unit increments.
The spider always moves towards the fly by one unit.
The fly:
  moves towards the spider by one unit with probability
  moves away from the spider by one unit with probability
  stays at its current location with probability .
  When the spider and the fly land in the same position or cross over each other, the spider captures the fly.
  IN PAC-MAN
  The idea can be replaced with the ghost acting as predator (spider) and pacman (who has uncertain movement compared to the ghost) acting as prey (fly). This allows us to implement a more aggressive ghost policy than the stochastic position (from his point of view) of Pac-Man.
  The idea could also be turned around by providing for the use of power-up for Pac-Man.
1
2
3
4
5
6
1
2
3
4
5
6

## Slide 11
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
PROBLEM FORMULATION
The artificial player will have to choose the direction in which to move by taking into account various objectives:
Minimize the number of steps useful for capturing all pills currently present;
Enact an escape policy the moment Pac-Man is below a critical distance from the ghost;
?
CONTROL STRATEGIES
CONTROL STRATEGIES
Check on the distance between the positions of the ghost and Pac-Man (by considering the Euclidean norm as a metric) and "critical distance" to implement an aggressive or escaping policy.
Choose whether escape from the ghost (MPC) or collect all pills (TRAVEL SALESMAN PROBLEM)
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 10
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 12
YALMIP
YALMIP is a MATLAB toolbox
YALMIP supports a wide range of optimization problems, including linear programming (LP), mixed-integer linear programming (MILP), quadratic programming (QP) and nonlinear programming (NLP).
It also provides a convenient framework for formulating and solving MPC problems, when there is need to define:
  the system
  the objective function to be optimized
  the constraints on the system variables
The YALMIP MPC formulation typically involves an optimization problem that is solved at each control interval to determine the optimal control inputs over a finite prediction horizon. In this context we used the GUROBI SOLVER!
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 11
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 13
MODEL PREDICTIVE CONTROL 1/2
Objective Function:
Escape from the ghost
Find and try to reach nearest pill
The prediction horizon was set at 3.
The large number of tests we performed​ consistently reported successes using the following weights​ α = 0.22, β = 0.11 that demonstrates the efficiency of the​ control strategy.
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 12
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 14
MODEL PREDICTIVE CONTROL 2/2
What about constraints? Three purposes:
Forcing Pac-Man remaining within the perimetral walls:
  upper bound
  lower bound
  left bound right bound
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 13
Optimization of Pac-Man strategies using Model Predictive Control
MATLAB IMPLEMENTATION CODE
Input's consistency:
Let Pac-Man avoids obstacles : MOST CHALLENGING!!

## Slide 15
MODEL PREDICTIVE CONTROL 2/2
What happens when strict inequality constraints are written in Yalmip code? This is the response:
Let Pac-Man avoids obstacles WHY «MOST CHALLENGING»?
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 14
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 16
MODEL PREDICTIVE CONTROL 2/2
Key idea to handle a inequality constraints:
Transform obstacle’s coordinates as a unique number according to this rule:
Let’s consider the first obstacle with coordinates
Then:
Example
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 15
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 17
MODEL PREDICTIVE CONTROL 2/2
Key idea to handle a inequality constraints:
Transform obstacle’s coordinates as a unique number according to this rule:
  Introduce symbolic binary variable related to the obstacle
  When the potential future Pac-Man’s coordinates correspond to location of the at the stage k+1, the following constraints allow to recognize this episode requiring both value of and equals to 1:
How to recognize an invalid pac man states evolution?
Example
  If Pac-Man is at the and the future coordinates will be equal to that of the first obstacle:
  Then the constraints would require both
  !!
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 15
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 18
MODEL PREDICTIVE CONTROL 2/2
Key idea to handle a inequality constraints:
Transform obstacle’s coordinates as a unique number according to this rule:
  Introduce symbolic binary variable related to the obstacle
  When the potential future Pac-Man’s coordinates correspond to location of the at the stage k+1, the following constraints allow to recognize this episode requiring both value of and equals to 1:
How to recognize an invalid pac man states evolution?
  Just make sure that the sum of and is never equal to 2!
How to avoid this situation?
Once recognized this unwanted situation it is avoided thanks to this constraint!
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 15
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 19
MODEL PREDICTIVE CONTROL 2/2
Let’s consider the first obstacle with coordinates
Then:
Example
If Pac-Man is at the and the future coordinates will be equal to that of the first obstacle:
Then the constraints would require both
!!
Once recognized this unwanted situation it is avoided thanks to this constraint!
Key idea to handle a inequality constraints:
Transform obstacle’s coordinates as a unique number according to this rule:
  Introduce symbolic binary variable related to the obstacle
  When the potential future Pac-Man’s coordinates correspond to location of the at the stage k+1, the following constraints allow to recognize this episode requiring both value of and equals to 1:
How to recognize an invalid pac man states evolution?
  Just make sure that the sum of and is never equal to 2!
How to avoid this situation?
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 15
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 20
MPC - ALTERNATIVE COST FUNCTION
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 16
Optimization of Pac-Man strategies using Model Predictive Control
An alternative for implementing this constraint was to take it into account as an objective function.
Where  represents the coordinates of the center of the obstacle represents the largest coefficient needed to make the constriants violation bad IN MATLAB:
Infeasible trajectory
Despite the weight in objective function, this does not allow us to be certain that the constraints are not violated.
Although there are matches in which the strategy works but there are some simulations and special cases that lead Pac-Man to make infeasible movements.
NOT A FEASIBLE SOLUTION !!!

## Slide 21
OPTIMIZATION PROBLEM: TRAVEL SALESMAN 1/4
The traveling salesman algorithm is a widely used method for solving combinatorial optimization problems in which a salesman must visit a set of cities while minimizing the total distance traveled.
This algorithm has been used to determine the optimal path that Pac-Man (salesperson) must follow to collect all the pills (cities).
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 17
Optimization of Pac-Man strategies using Model Predictive Control

## Slide 22
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 18
Optimization of Pac-Man strategies using Model Predictive Control
OPTIMIZATION PROBLEM: TRAVEL SALESMAN 2/4
Weight coefficients are calculated using the Euclidean norm.
STEP 1: SUBTOUR GENERATION
Constraint that each stop is present in exactly two trips.
The decision variables are binary and associated with each trip:
1 represents an existing trip on the tour
0 represents a trip not on the tour.
Objective function:

## Slide 23
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 19
Optimization of Pac-Man strategies using Model Predictive Control
OPTIMIZATION PROBLEM: TRAVEL SALESMAN 3/4
subsequent approximations of the tour
STEP 2: SUBTOUR REDUCTION

## Slide 24
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 20
Optimization of Pac-Man strategies using Model Predictive Control
OPTIMIZATION PROBLEM: TRAVEL SALESMAN 4/4
Trips corresponding to the active decision variables are taken and reordered. The first trip will have Pac-Man’s location as its start, all subsequent trips are selected to ensure that the end point of one trip matches the start point of the next trip.
STEP 3: SUBTOUR REDUCTION

## Slide 25
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
CONTROL STRATEGIES IN MARKOV CHAIN’S IDEA
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 21
Optimization of Pac-Man strategies using Model Predictive Control
Example of solving with Policy iteration: a similar problem from «Reinforcement Learning: An Introduction»:
Another solution from literatures:
Design of Pac-Man Strategies with Embedded Markov Decision Process in a Dynamic, Non-Deterministic, Fully Observable Environment, Jiachang (Ernest) Xu
Example 4.1 from Reinforcement Learning: An Introduction

## Slide 26
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 22
Optimization of Pac-Man strategies using Model Predictive Control
SIMULATION RESULTS
WIN
WIN
WIN
WIN
WIN
WIN

## Slide 27
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 23
Optimization of Pac-Man strategies using Model Predictive Control
FUTURE DEVELOPMENTS
It is important to note that our work is not limited only to the game of Pac-Man, but can be extended to other
similar games or control problems in wider contexts. The control techniques used can be applied to a wide range of scenarios, contributing to the development of intelligent and autonomous solutions.
The next challenges that might come are:
Implementation of additional and detailed game features;
Extension in multi-agent environment;
Improve the efficiency of control strategies and reduce computational load;
Portability of control strategy on different problems;
Application of control implementation to a real problem;
AND MUCH MORE…

## Slide 28
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 24
Optimization of Pac-Man strategies using Model Predictive Control
REFERENCES
Francesco Borrelli, Alberto Bemporad, and Manfred Morari. Predictive control for linear and hybrid systems. Cambridge University Press, 2017.
Luigi Glielmo, An Introduction to Optimization, Università di Napoli Federico II, lecture slides. Mar. 2023.
https://yalmip.github.io/example/standardmpc/
Mathworks, Traveling Salesman Problem: Solver-Based URL:https://it.mathworks.com/help/optim/ug/travellingsalesman-problem.html
Andrea Morghen, Antonio Gargiulo, Valentina Giannotti, Emmanuel Grimaldi. PAC-MAN vs. MATLAB. https://github.com/ValentinaGiannotti/Pac-Man-, Universita di Napoli Federico II, May. 2023.
ImageProcessingToolbox https://it.mathworks.com/help/images/
Design of Pac-Man Strategies with Embedded Markov Decision Process in a Dynamic, Non-Deterministic, Fully Observable Environment, Jiachang (Ernest) Xu

## Slide 29
Gargiulo – Giannotti – Grimaldi – Morghen University of Naples Federico II – July 2023
SLIDE 19
Optimization of Pac-Man strategies using Model Predictive Control
Title